## Slide 1
⚙
Bearing Fault Diagnosis
MIC-300: Lab Based Project | Spring 2025-26
Department of Mechanical and Industrial Engineering, IIT Roorkee
Multi-Objective Clustering with Feature Sparsity
for Bearing Fault Diagnosis
Students:
Advik Goyal | [Team Member 2] | [Team Member 3]
Supervisor:
Prof. [Supervisor Name]
March 2026
NSGA-II
Unsupervised Learning
CWRU Dataset
Pareto Optimisation
Feature Selection
IIT Roorkee

## Slide 2
Problem Definition
Why do bearing faults matter — and why is this hard?
40–50%
of rotating machine failures from bearings
4 Fault Types
Normal · IR · Ball · OR @ 4 severity levels
4 Load Conds.
0–3 HP | 1730–1797 RPM masks fault signatures
7 Features Extracted
RMS, Kurtosis, Skewness, Crest, P2P, Std, Spec.Centroid
Challenge 1: Load-Condition Artefacts
▸ Different motor loads (0–3 HP) shift vibration amplitude
▸ Global normalisation fuses load variation with fault signatures
▸ Fix: per-load-condition StandardScaler before merging
Challenge 2: Class Imbalance
▸ OR fault has 3 mounting positions (@3, @6, @12) → 3× more data
▸ Biases the clustering objective toward the over-represented class
▸ Fix: Random undersampling to median class count
Challenge 3: No Ground-Truth for Clustering
▸ Bearing fault diagnosis is inherently unsupervised at deployment
▸ Labels only available for validation — not used during optimisation
▸ Evaluation: Adjusted Rand Index (ARI) + Silhouette Score
Challenge 4: Competing Objectives
▸ Tight clusters ≠ well-separated classes (compactness vs. separation)
▸ More features ≠ better clusters (curse of dimensionality)
▸ Solution: 3-objective Pareto optimisation (f1, f2, f3)
2

## Slide 3
Research Objectives
A rigorous multi-objective framework for unsupervised fault discovery
RO 1
Dataset Pipeline
Build a robust preprocessing pipeline: per-load-condition normalisation · class balancing · 16-class severity labelling → 7,335 balanced samples from 12k Drive-End CWRU dataset
RO 2
Chromosome Encoding
Design a unified variable-length chromosome: [ K ] [ K×D cluster centres ] [ D-bit feature mask ] → 78 variables representing K ∈ {2…10}, D = 7 features, simultaneous K + feature selection
RO 3
Three-Objective NSGA-II
Simultaneously minimise: f1 Compactness (TWCSS/N/d) · f2 Connectedness (kNN cross-cluster fraction) · f3 Simplicity (L0 feature count) → 200-population × 200-generation NSGA-II with hybrid initialisation
RO 4
Pareto Analysis & Validation
Extract Pareto front → knee-point selection via normalised Chebyshev distance Validate against ground-truth: ARI (4-class fault type) + ARI (16-class type × severity) → Silhouette Score as internal cohesion metric
RO 5
Physical Interpretation
Map discovered minimal feature subsets to bearing fault physics Identify which vibration statistics (RMS, Kurtosis, Spectral Centroid…) catch which fault modes → BPFI / BPFO / BSF marker validation via FFT analysis
3

## Slide 4
Methodology
Three-stage pipeline: Data → Optimisation → Interpretation
① Data Pipeline
CWRU 12kHz .mat files
12k Drive-End, 4 fault types, 4 sizes, 4 loads
Segment → Windows (n=1024)
Extract fixed-length segments, compute 7 features/window
Per-load StandardScaler
Separate normaliser per load condition (FIX-1)
Random Undersampling
Balance to median class count (FIX-2)
16-class composite label
fault_type × fault_size — for ARI validation (FIX-3)
▶
② NSGA-II Optimisation
Chromosome:
[ K | C₁…C_K×D | mask₁…mask_D ] (78 vars)
Population:
200 individuals | Hybrid init: KMeans + random
Objectives:
f1 TWCSS/N/d · f2 kNN-penalty · f3 L0-norm
Operators:
SBX + 1-pt crossover | Polynomial + bit-flip mutation
Budget:
200 generations → Pareto front (200 solutions)
▶
③ Analysis
Knee point
Min Chebyshev dist. to ideal in norm. space
Validation
ARI (4-cls + 16-cls) Silhouette Score
Interpretation
Feature mask → physics FFT + fault freq. markers
Three Objectives Simultaneously Optimised by NSGA-II
f₁ Compactness
min TWCSS / (N · d_active)
Total within-cluster sum of squares — measures how tightly grouped the data is
f₂ Connectedness
min Σ penalty(xᵢ, kNN(xᵢ))
Fraction of k nearest-neighbours that lie in a different cluster
f₃ Simplicity
min ‖mask‖₀ ∈ {1…7}
L0-norm of feature mask — forces the algorithm to use as few features as possible
4

## Slide 5
Project Timeline
MIC-300 | Semester: November 2025 – May 2026
Nov '25
Dec '25
Jan '26
Feb '26
Mar '26
Apr '26
May '26
Literature Review & Dataset Acquisition
Done
CWRU Preprocessing Pipeline (FIX 1-3)
Done
Chromosome Encoding & NSGA-II Framework
Done
v1 Pipeline Run & Pareto Analysis
Done
v2 Bug Fixes & Full Dataset Re-run
Done ✓
Mechanical Interpretation & Visualisations
Done ✓
Comparative Analysis & Insights Documentation
In Progress
End-term Write-up & Final Report
Upcoming
Completed
In Progress
Upcoming
Current Period
5

## Slide 6
Work Done So Far — Part 1
Dataset preparation, bug fixes and algorithm implementation
A CWRU Dataset v2 — Three Critical Fixes Applied
7,335
Balanced samples
12
Classes (16-class)
7
Features extracted
4
Fault types
28
OR files loaded
4
Load conditions
FIX 1: Per-Load Normalisation
▸ Old: single global StandardScaler mixed load variation with fault signal
▸ New: separate scaler per load condition (0, 1, 2, 3 HP) before merging
▸ Impact: primary driver of ARI improvement — load artefacts no longer dominate
FIX 2: Class Balancing
▸ OR fault had 3 mounting positions → 3× more segments than other classes
▸ Random undersampling to median class count across all 4 fault types
▸ Impact: prevents the clustering from being biased towards OR
FIX 3: OR Recursive Glob + 16-class Labels
▸ Bug: non-recursive glob missed OR/007/@3/, @6/, @12/ subdirectories
▸ Fix: glob(..., recursive=True) now loads all 28 OR files (was 4)
▸ Severity label: fault_type × fault_size → 12 distinct classes for ARI-16
B NSGA-II Implementation Highlights
Hybrid Init
1/3 KMeans-seeded + 1/3 random data-point centres + 1/3 pure random
Custom Crossover
SBX on continuous centre genes + 1-point crossover on 7-bit feature mask
Custom Mutation
Polynomial mutation + bit-flip (p=0.15) + structural K±1 (p=0.1)
History Callbacks
Snapshots at gens {1,5,10,20,35,50,75,100,150,200} for convergence study
6

## Slide 7
Work Done So Far — Part 2
NSGA-II results, Pareto front analysis and physical interpretation
0.36
ARI (4-class) fault type
0.50
ARI (16-class) type×severity
0.82
Silhouette Score
200
Pareto Solutions
1–2
f3 active features
RMS
Dominant feature
Pareto Front Analysis
Solution type
K
Features
ARI (4cls)
Knee point
10
RMS
0.3595
Best ARI
10
RMS
0.3595
Most compact
10
RMS
0.2904
f3=2 example
5
RMS + Kurtosis
0.3102
Physical Interpretation
▸ RMS dominates
After per-load normalisation, overall energy level (RMS) is the single most discriminative feature — confirming that fault-induced energy changes are the primary clustering signal.
▸ f3 Pareto range: 1–2 features
Adding features beyond RMS does not improve cluster quality. Curse of dimensionality: 7 features all similarly discriminative → sparse is better in this 7-dimensional space.
▸ 16-class ARI > 4-class ARI (0.50 vs 0.36)
Clusters align more closely with fault_type × severity than fault_type alone — the algorithm discovers severity sub-structure even without severity labels during training.
v1 → v2 Comparison:
Dataset: 5,678 → 7,335 samples | OR files loaded: 4 → 28 | Silhouette: 0.838 → 0.815 | Note: lower ARI in v2 reflects harder, more realistic clustering (full OR class variation)
7

## Slide 8
Live Demonstration — Interactive 3-D Pareto Front
pareto_3d_interactive.html
Drag to rotate
Fully rotatable 3-D scatter of all 200 Pareto solutions
Hover for details
Each point shows: K, active features, ARI, Silhouette, f1/f2/f3 values
Red ◆ = Knee point
Minimum Chebyshev distance to ideal — best balanced solution
Gold ■ = Best ARI
Solution with highest Adjusted Rand Index vs. fault labels
Colour = ARI
Green → higher ARI (better fault alignment), Red → lower ARI
Axes
f1 Compactness × f2 Connectedness × f3 Simplicity (# features)
Open moc_results_v2/pareto_3d_interactive.html in any browser — no server required
8